## Slide 1: OpenMeasure: Adaptive Flow Measurement & Inference with Online Learning in SDN
Chang Liu
Robust & Ubiquitous Networking Lab
http://www.ece.ucdavis.edu/rubinet
ELECTRICAL &
COMPUTER ENGINEERING

## Slide 2: Network Measurement & Inference
Fine-grained traffic size information provides an essential input for many network design and operation tasks.
  Capacity planning, network provisionning, load balancing, anomaly detection
Flow size can be measured directly or inferred indirectly from sampled statistics.
  Challenge of direct flow measurement: scalability, limited measurement resouces
  Estimate TM (traffic matrix) using network inference techniques

## Slide 3: SDN based Measurement & Inference
Software-Defined Networking (SDN)
  Decouples the network control and forwarding functions
  Enables dynamic/re-configurable network control
  Provide global view of network
New opportunities
  Optimal measurement resource allocation
    Dynamically determine what/when/where to measure
  Assist network inference with online learning
    Dynamically decide what observations to obtain and which missing entries to measure
Rules
Statistics
Actions
Controller
Flow Table(s)
Secure Channel
Rules/Actions
Statistics

## Slide 4: OpenMeasure
A network-wide adaptive flow measurement and inference framework with continuous learning capability
  Assist network inference with online learning predictions and dynamically update the measurement rules network-wide to track and measure the most informative flows
  Leverage the global view of SDN controller to optimally place flow monitoring rules across network

## Slide 5: OpenMeasure
System model
  A centralized controller
  Subset of switches are SDN enabled
  SDN switches are pre-populated by default routing rules
  A handful of TCAMs available for installing new measurement rules
Controller
Design Rules
Install Rules
Collect Statistics
Estimate TM
1
2
3
4
Flow: <srcIP,dstIP>

## Slide 6: Problem Formulation
Definitions
Example

## Slide 7: Problem Formulation
Compressive Sensing Estimation*
[1] M. Malboubi, L. Wang, C. Chuah, and P. Sharma, “Intelligent SDN based traffic (de)aggregation and measurement paradigm (iSTAMP),” IEEE INFOCOM, 2014.
Multi-point
Single-point
Our approach: Use the K available TCAM entries to sample K most informative flows

## Slide 8: Our approach: OpenMeasure
Key components
  Identify the most informative flows from online learning and generate candidate rules to install
  Dynamically determine where/what rules are to be installed network-wide using global view
  Collect aggregate & flow statistics from switches and perform TM estimation
Controller
Design Rules
Install Rules
Collect Statistics
Estimate TM
1
2
3
4
Flow: <srcIP,dstIP>

## Slide 9: Rule Design
Adaptive mechanism with online learning
At each time epoch, update flow tables to track and measure K most informative flows
  Measuring the most informative flows is important for improving TM estimation accuracy
  Identify large flows with online learning algorithm
  Weighted Linear Prediction (WLP)
  Modified Upper Confidence Bound (MUCB) Prediction (MUCBP)

## Slide 10: Weighted Linear Prediction (WLP)
Maintain a list of n records for each flow
The predicted flow size is a weighted linear sum of history records
  Rank flows in decending order of predicted flow sizes and select a set of candidate large flows to track and measure in the next time epoch

## Slide 11: Modified Upper Confidence Bound (MUCB) Prediction
Take flow size of a directly measured flow as sampling reward
Maximize total reward from all available TCAMs over time
  Multi-armed bandit (MAB) sequential resource allocation
  Balance between exploration and exploitation

## Slide 12: Bootstrap with MLRF
Initial system dynamics
  Maximum Load Rule First (MLRF)* strategy to populate the initial measurement rules
  The load of a rule is defined as the number of flows matching the rule in an SDN switch
  Start from rule w/ maximum load
  Generate a new rule with balanced load
  Increase the priority of new rule
[2] Y. Gong, X. Wang, M. Malboubi, S. Wang, S. Xu, C.N. Chuah, "Towards Accurate Online Traffic Matrix Estimation in Software-Defined Networks", ACM SIGCOMM SYMPOSIUM ON SDN RESEARCH (SOSR), 2015.
Old Rule w/ priority p
New Rule w/ priority (p+1)

## Slide 13: Rule Placement
Determine where (which switch) to directly measure what (which flows)
Optimize rule placement network-wide with the controller’s global view

## Slide 14: Rule Placement
The problem can be formulated into an integer linear program (ILP)
  Computational complexity increases exponentially as the size of the network increases
A flow can only be measured at an SDN switch that it passes in its routing path.

## Slide 15: Rule Placement
The problem can be formulated into an integer linear program (ILP)
  Computational complexity increases exponentially as the size of the network increases
An SDN switch with Ki available TCAMs can sample Ki flows at most.

## Slide 16: Rule Placement
The problem can be formulated into an integer linear program (ILP)
  Computational complexity increases exponentially as the size of the network increases
A flow will not be per-flow measured more than once.

## Slide 17: LastHop placement algorithm

## Slide 18: LastHop placement algorithm

## Slide 19: LastHop placement algorithm

## Slide 20: Greedy placement algorithm
3
2

## Slide 21: Greedy placement algorithm
3

## Slide 22: Performance Study
Network Topologies
  Geant (23 nodes & 37 links)
  A hybrid SDN-network with 6/23 nodes set to be OF switches
  Routing entries are generated based on shortest-path routing
Data Sets
  Real traffic traces from Geant are used
  Randomly assign a number of IP prefixes to each node to get fine-grained traffic matrices
Performance Metrics
  Accuracy for TM estimation: Normalized Mean Square Error (NMSE)
  Performance for HHH identification: Recall & Precision

## Slide 23: Accuracy for TM Estimation
Normalized Mean Square Error (NMSE)
Compare OpenMeasure with
  Random Scheme (RS): Randomly sample a set of flows
  Static Aggregation (SA): Fixed grouping of flows
  LFF*: Measure a static set of large flows based on one-shot learning
[2] Y. Gong, X. Wang, M. Malboubi, S. Wang, S. Xu, C.N. Chuah, "Towards Accurate Online Traffic Matrix Estimation in Software-Defined Networks", ACM SIGCOMM SYMPOSIUM ON SDN RESEARCH (SOSR), 2015.

## Slide 24: Single-Point: Learning important flows
OpenMeasure(WLP): Apply WLP learning algorithm in rule design
OpenMeasure(MUCBP): Apply MUCBP learning algorithim in rule design
Accuracy gain from continuous learning
WLP slightly outperforms MUCB
Accuracy gain from learning

## Slide 25: Multi-Point: Accuracy for TM Estimation
Accuracy gain from adaptive measurement with SDN-enabled online learning
OpenMeasure(WLP/MUCBP+GRP): Apply WLP/MUCBP learning algorithm in rule design and Greedy rule placement (GRP) in rule placement.
r = # of TCAM entries
# of flows

## Slide 26: Accuracy for TM Estimation
r = # of TCAM entries
# of flows
Accuracy gain from continuous learning
OpenMeasure(WLP+GRP/LRP): WLP learning algorithm in rule design and Greedy rule placement (GRP)/LastHop rule placement algorithm in rule placement
OpenMeasure(WLP+ILP): WLP learning algorithm in rule design and optimally solve the ILP in rule placement
Two heuristic algorithms achieve estimation accuracy close to that of optimal solution

## Slide 27: Hierarchical Heavy Hitter (HHH) Detection
Detecting HHHs is important for security applications
  Pinpointing DoS and DDoS attacks, discovering worms and anomalies
Build a prefix tree of source IP addresses for each destination node
HHHs in shaded circles

## Slide 28: Hierarchical Heavy Hitter (HHH) Detection
Recall: total number of true HHHs detected over real number of HHHs
Precision: total number of true HHHs detected over the total number of HHHs reported
Measurements with SDN-enabled online learning provides the highest precision and recall

## Slide 29
Thank you!